## Slide 1
VIVEK SINGH
VLSI Physical Design | RTL-to-GDSII | EDA Tools

## Slide 2
VIVEK SINGH
Open-Source DFT + Physical Design Flow
MAC System Top | AXI4-Lite + FIFO + 2×2 MAC Array
Nirma University
B.Tech EIE + VLSI Minor
PDK
gpdk090
GitHub
exoticallyvivek
vr.singh1612@gmail.com

## Slide 3
Project Overview — MAC Accelerator IP
What was built, why, and the full toolchain
VIVEK SINGH
All Rights Reserved
vr.singh1612@gmail.com
What Was Built
MAC Accelerator IP — sky130A
AXI4-Lite slave interface — register-mapped CPU access
Synchronous FIFO (16×32-bit) — operand buffering
2×2 MAC Array — 4 parallel multiply-accumulate units
5-stage pipelined MAC unit — Booth encoder + Wallace tree
Output register bank — stable results until CPU reads
Control FSM — orchestrates full data flow end-to-end
Project Objective
Demonstrate a complete RTL → DFT (ATPG + JTAG) → Physical Design (RTL-to-GDSII) flow using a 100% open-source EDA toolchain on an industrial-complexity design with AXI interface, FIFO, and pipelined MAC array on sky130A 130nm PDK.

## Slide 4
MAC System Top — Architecture Overview
Block diagram: CPU → AXI → FIFO → MAC Array → Output Regs → CPU
VIVEK SINGH
All Rights Reserved
vr.singh1612@gmail.com
mac_system_top
CPU /
Host
AXI Master
→
AXI4-Lite
Slave
5-ch protocol
Reg map
→
Control
FSM
5-state
orchestrator
→
Sync
FIFO
16×32-bit
packed A,B
→
2×2 MAC
Array
4 MAC units
parallel
→
Output
Reg Bank
Stable results
for AXI read
← AXI Read path: CPU reads results via RDATA register
End-to-End Data Flow
① CPU writes operand A (16-bit) to AXI reg 0x00, operand B to 0x04, then asserts START at 0x08
② AXI slave latches A,B and pulses axi_mac_start; Control FSM packs {A,B} → 32-bit word into FIFO
③ FSM pops FIFO (rd_data = {A[31:16], B[15:0]}), asserts mac_valid_in — triggers MAC computation
④ MAC Array: selected MAC unit (via mac_sel[1:0]) runs 5-stage pipeline → product arrives at accumulator
⑤ Output Register Bank captures result_valid pulse → stores result → asserts done_flag
⑥ CPU polls status reg 0x1C (DONE=1), then reads results from 0x0C–0x18 via AXI read channel

## Slide 5
Block Detail — AXI4-Lite Slave & Control FSM
Register-mapped interface + orchestration state machine
VIVEK SINGH
All Rights Reserved
vr.singh1612@gmail.com
AXI4-Lite Slave Interface
Purpose: Bridge CPU ↔ MAC System via memory-mapped registers
How it works:
5-channel AXI4-Lite: AW (write addr), W (write data), B (write resp), AR (read addr), R (read data)
Write FSM: WR_IDLE → WR_DATA → WR_RESP — accepts AWADDR, latches data, sends OKAY
Read FSM: RD_IDLE → RD_DATA — multiplexes result registers onto RDATA bus
mac_start is a 1-cycle pulse generated on WDATA[0] write to 0x08
Register Map
0x00 Operand A (write)
0x04 Operand B (write)
0x08 Control: START|RST|SEL[1:0]
0x0C–0x18 Results MAC0–MAC3 (read)
0x1C Status: BUSY|DONE|FULL|EMPTY
Control FSM — 5 States
Purpose: Sequence FIFO push → pop → MAC trigger → done
IDLE
Wait for axi_mac_start; latch mac_sel from AXI control reg
↓
PUSH
Data pushed to FIFO combinatorially; wait for !fifo_empty
↓
COMPUTE
Assert fifo_rd_en to pop; mac_valid_in → starts 5-stage MAC pipe
↓
POP
Deassert valid; check if more data in FIFO → loop or go DONE
↓
DONE
Clear busy_reg; assert done_reg; return to IDLE for next transaction
Key signal: orb_done (from output reg bank) → signals FSM operation complete

## Slide 6
Block Detail — Sync FIFO & 2×2 MAC Array
Operand buffering and parallel multiply-accumulate
VIVEK SINGH
All Rights Reserved
vr.singh1612@gmail.com
Synchronous FIFO (16 × 32-bit)
Purpose: Buffer operand pairs from AXI writes; decouple CPU write speed from MAC pipeline
How it works:
Depth=16, Width=32 — stores packed {A[15:0], B[15:0]} pairs
Circular buffer: wr_ptr & rd_ptr each 5-bit (extra bit for full/empty detect)
count = wr_ptr − rd_ptr → full when count==16, empty when count==0
almost_full (count==15) and almost_empty (count==1) status flags
2×2 MAC Array — 4 Parallel MAC Units
Purpose: Parallel multiply-accumulate — selected MAC runs independently
How it works:
All 4 MACs receive same A,B inputs from FIFO
mac_sel[1:0] decoder: 00=MAC0, 01=MAC1, 10=MAC2, 11=MAC3
Only selected MAC gets en=1 (valid_in); others idle
Each MAC accumulates independently — useful for GEMM
MAC0
(00)
MAC1
(01)
MAC2
(10)
MAC3
(11)
← A, B (from FIFO)
result_mac0..3 →

## Slide 7
Block Detail — 5-Stage Pipelined MAC Unit
Booth encoding → Wallace tree → CPA → Accumulator
VIVEK SINGH
All Rights Reserved
vr.singh1612@gmail.com
S1 — Input Reg
Register A,B
+ valid_in
Every cycle
→
S2 — Booth
Encoder
9 partial
products
Signed 16×16
→
S3 — Wallace
L1+L2
3×CSA → 6
2×CSA → 4
intermediate
→
S4 — Wallace
L3+CPA
CSA → 3
Ripple CPA
32-bit product
→
S5 — Accum-
ulator
acc+=product
rst_acc clears
result_valid
Booth Encoder (Stage 2)
Sign-extended A: {{16{A[15]}}, A} — handles negative numbers
Generates 8 partial products pp0..pp7 by shifting A by B[i]
pp7 merges B[7..15] including 2's complement sign bit (B[15]: negate)
pp8=0 placeholder — 9 PPs total for Wallace tree
Wallace Tree + Accumulator (S3–S5)
L1: 3×CSA_32 reduce 9 PPs to 6 values (sum+carry pairs)
L2: 2×CSA_32 reduce 6 to 4; carry shifted left 1 bit (weight align)
L3+CPA: final CSA + ripple adder → 32-bit product
Accumulator: acc = acc + product on valid; rst_acc clears for new op

## Slide 8
VIVEK SINGH
All Rights Reserved
vr.singh1612@gmail.com
7

## Slide 9
VIVEK SINGH
All Rights Reserved
vr.singh1612@gmail.com
8
Thank You
vr.singh1612@gmail.com | +91-82389-14028 | Nirma University, Ahmedabad